## Slide 1: SALTS (Submersible Acoustically Linked Transmission System)
by James King, Patrick Cunniff, Stephen MacKinnon, Colemann Johnston, Ryan Penny, and Rafal Premik

## Slide 2: Problem Summary
Goal:
  Transmit video underwater in near-real time
  Design and build a robot capable of housing the video transmission system and maneuvering underwater

## Slide 3: Why we tried to solve this problem.
Harbor security/surveillance
Better AUV mobility in hostile environments
Ability to communicate underwater without surfacing
Target tracking and identification
New exploration opportunities
Proof of concept for sonar video transmission

## Slide 4: System Overview
Base Station
Mobile Unit

## Slide 5: Robot Overview
Fully Holonomic Drive
All parts delivered
have been successfully
test-fit
Pressure vessel seals
have been designed
and documented -
but not manufactured
by the machine shop

## Slide 6: Robot Assembly To Do
Bottom of pressure bucket needs to be drilled for cable holes and then glued to the electronics assembly
Lids need to be machined
Mineral oil needs to be selected and tested
Troubleshoot the transducer gimbal

## Slide 7: Motion Control
DSPIC33FJ64GS610-I-/PF
  Processing Unit
  16 bit architecture
  100 pin package
  18 PWM outputs
  Two I2C ports
  Fixed Point DSP
    PID
    Inertial Processing

## Slide 8: Robot Electronics - Sensor Feedback
MPU-6050QFN 6-axis accelerometer
  Communicated via I2C

## Slide 9: Robot Electronics - Motor Control
H-Bridge LM18200T
12 populate the robot control board
2 are used for each stepper motor

## Slide 10: Robot Electronics - To Do
Solve major I2C driver issue that causes MPU to hang.
Get final assembly together for pool testing and PID loop tuning.
Determine a method for remote programming/tuning while in the water.
Better define the interface between PIC and BeagleBoard.

## Slide 11: Communication System

## Slide 12: Why we chose USRP/GNURadio
Initially wrote our own OFDM code
  C++, based on pre-existing Matlab code
Opted to use GNU Radio after we were given 2 USRPs
  More reliable, robust code
  Easy to modify (Python, C++)
  Community support
Disadvantage: OFDM not a large community action item so less support really exists for our use case.

## Slide 13: Specs
Ettus Research USRP1
  Capable of DC - 6 GHz TX/RX
  Two dual 64 MS/s 12-bit ADCs
  Two dual 128 MS/s 14-bit DACs
  Up to 16 MS/s USB Streaming
  Altera Cyclone FPGA
GNU Radio
  Free, open-source
  Easy-to-use, easy-to-modify signal processing blocks
BeagleBoard-xM
  More than 2,000 Dhrystone MIPS
  C64+ TMDSP core
  512MB LPDDR RAM

## Slide 14: OFDM
OFDM used to best utilize our bandwidth
Guard intervals used to resolve multipathing and reduce intersymbol interference
Cyclic prefix for redundancy

## Slide 15: Modulation
QPSK modulation used, though DQPSK would be ideal to sync phases
Other modulation schemes were tested and worked - low-M PSK best for ocean-like channels

## Slide 16: Compression & Bit Errors
1st draft - Text File
2nd draft - BMP Image
3rd draft - H264 Video
DSP or CPU encoding
Bit errors very small (excluding GNU Radio bugs) and H264 is pretty resilient to errors
10-3 - 10-4 when tested with Rameez

## Slide 17: Data Rates for Live Video
Xducers bandwidth = 15 kHz
Our data rate limit (-packets loss) = 30 kbps
Video data rate achieved = 29kbps
(5fps, 160x120px, low quality)
CRC & cyclic prefix - minimal overhead
GNU Radio - maximal overhead

## Slide 18: Amplifier
Needs to be fairly efficient and designed for linear operation.
Multistage amplifier required to isolate load from filtering.
20V/us slew rate amps required
Must be able to drive capacitive loads (transducer)
Any added filtering should have linear phase over the band (Bessel filter)

## Slide 19: Tx/Rx Switch
A Tx/Rx switch must be designed to protect the receive path from possible high power exposure as well as to accommodate simplex communication.
Initial attempts at a switch sufficiently protected the receiver path, but loaded down the received signal. Further design revisions must be implemented.

## Slide 20: Filtering
A fourth order Bessel
filter is implemented,
which provides a
flat group delay over
the frequency band.
This prevents a non-
linear frequency
dependent spreading
of the signal in the
time domain.

## Slide 21: Automatic Gain Amplifier
To further condition the received signal, an AGC may be added to the signal path to appropriately balance the incoming signal. This will be essential when transmitting over longer distances.
AGC implementation will present several design challenges such as signal envelope detection, as well as DC biasing circuit.

## Slide 22: Power Board/Requirements
+/- 18V@2 for the amplifiers
+3.3V@1A for PIC
+5V@2A for BeagleBoard
+6V@3.5A for the USRP
+12V@30A for all motors
Note: This needs to be a PCB spin since it won't fit in the robot as a breadboard.

## Slide 23: Budget Totals
Robot Mechanicals | $2141
Robot Electronics | $678
Communication Host | $150
Communication Analog Front End | Donated ($1400)
Communication Amplifier | $100
Camera | $25
Power Supply | $35
Totals | $3129 ($4529)

## Slide 24: Accomplishments
Underwater communication successful. Rate and distance things to work on.
Nearly complete underwater robot design assembled. Iteration will assist in robustness and completeness.
Early Amplifier & Filtering completed.
Learned a ton.

## Slide 25: Shortcomings
SPI jitter
Fixing GNU radio takes a long time
Unable to conduct a full pool test
Transducer bandwidth was much narrower than communicated
Major delays in machined parts delayed robot control troubleshooting as well as a full pool test

## Slide 26: If we were to do it again
Greater modularity. Too much was happening on one device (BeagleBoard).
Larger pressure vessel or better batteries so there can be in pool prototyping.
Utilize just the USRP devices and not GnuRadio with our own code.

## Slide 27: Thanks to:
Prof. Salehi
Prof. Shafai
Prof. Stojanovic
Rameez Ahmed
Kurt Braun and Michael MacNeil
Materials Systems Incorporated - Transducers
Sue Ekizian

## Slide 28: ROBOT Safety Scout!